| Datum Date Datum | 04.12.2003 | SERVICE INSTRUCTION | Model Modell Model | DRILLS ACU.ELECTRIC DRILLS |
| --- | --- | --- | --- | --- |
| Stran Page Seite | 1/1 |  |  |  |

REGULATION ABOUT RUNOUT OFF CHUCK BY DRILLS AND

ACU. ELECTRIC DRILLS

The machine has to be firmly put in the test holder. Control spine has to be put in the chuck in the whole length of the jaw but not to the bottom of the chuck. The chuck has to be pulled tight. Measuring watch indicator has to be put in contact with control spine. The drill has to be put on and at lowest possible speed of the spindle the measurement of the runout of the drilling head has to be performed. Maximal allowed runout of the drilling head is 0,25 mm

Product Type of test Testing equipment Allowed runout in mm Distance in mm DRILLS Runout of drilling head Measuring watch, Control spines M112747 Ø10 M112746 Ø13 M112889 Ø16 0,25 25 ACU.ELECTRIC DRILLS Runout of drilling head Measuring watch, Control spines M112747 Ø10 M112746 Ø13 0,43 25