| Datum Date Datum | 24.04.2006 | SERVICE INSTRUCTION | Model Modell Model | HSW 114,115,125,126 HSW 300/3000 |
| --- | --- | --- | --- | --- |
| Stran Page Seite | 1/1 |  |  |  |

PLACING OF THE BEARING ON ARMATURE FOR

HSW 114/115/125/126 AND HSW 300/3000

- Bearing on collector side of the armature is levelled with end of the armature shaft.

- Bearing on the fan side is placed together with pinion and washers between them. Measure A on drawing bellow is placing measure of the pinion (from top of the pinion to the end of the shaft).

- HSW 114, 115, 125, 126

  - measure A = 146.95 mm, between pinion and bearing are two washers :  17.302.218 (ø11,8/ø7,1X1) and 17.302.302 (ø11,8/ø7,1X0,3)

- HSW 300/3000

  - measure A = 157.9 mm, between pinion and bearing are two washers :  17.302.218 (ø11,8/ø7,1X1) and 17.302.508 (ø11/ø7,1X0,5)